## Slide 1: Semiconductor Chips
FPGA & CPLD
ASICs
Application Specific
Integrated Circuits
Microprocessors
Microcontrollers

## Slide 2: FPGA Principles
A Field-Programmable Gate Array (FPGA) is an integrated circuit that can be configured by the user to emulate any digital circuit as long as there are enough resources
An FPGA can be seen as an array of Configurable Logic Blocks (CLBs) connected through programmable interconnect (Switch Boxes)

## Slide 3
FPGAs Classifications
Implementation Architecture
Logic Implementation
Interconnect Technology
Symmetrical Array
Row based Array
Hierarchial PLD
Sea of Gates
Look Up table
Multiplexer based
PLD Block
NAND Gates
Static Ram
Antifuse
E/EPROM
FPGA types

## Slide 4: FPGA Advantages
Very fast custom logic
  massively parallel operation
Faster than microcontrollers and microprocessors
  much faster than DSP engines
More flexible than dedicated chipsets
  allows unlimited product differentiation
More affordable and less risky than ASICs
  no NRE, minimum order size, or inventory risk
Reprogrammable at any time
  in design, in manufacturing, after installation

## Slide 5: Manufacturers
Xilinx
Altera
Lattice
Actel
We will work with XILINX FPGAs

## Slide 6
.June 2011
The 4 biggest FPGA producers are :
Xilinx 2.4 Billion$ in 2011 49% of US mrket
Altera 40% 1. Billion955
Quick Logic 1% 26 Million$
MicriSemi 4% 207 Million $
Lattice Semi 6% 297 Million
Xilinx and Altera have 89% of the Market
With the top two FPGA companies taking up 89% of the FPGA market, you can be forgiven for thinking there was no one else out there. Xilinx and Altera have done a good job of defending the duopoly but a few companies are gradually winning market share by targeting specific applications

## Slide 8
Row-based
Interconnect
Logic Block
PLD Block
Interconnect
overlayed
on Logic
Blocks
Logic
Block
Interconnect
Sea-of-Gates
Hierarchical PLD
Interconnect
Symmetrical Array
Classes of common commercial FPGA
Various Block Architecture & Routing Architecture

## Slide 9
Company | General Architecture | Logic Block Type | Programming Technology
Xilinx | Symmetrical Array | Look-up Table | Static RAM
Actel | Row-based | Multiplexer-Based | Anti-fuse
Altera | Hierarchical-PLD | PLD Block | EPROM
Plessey | Sea-of-Gates | NAND-gate | Static RAM
PLUS | Hierarchical-PLD | PLD Block | EPROM
AMD | Hierarchical-PLD | PLD Block | EEPROM
QuickLogic | Symmetrical Array | Multiplexer-Based | Anti-fuse
Algotronix | Sea-of-gates | Multiplexers & Basic Gate | Static RAM
Concurrent | Sea-of-gates | Multiplexers & Basic Gate | Static RAM
Crosspoint | Row-based | Transistors Pairs & Multiplexers | Anti-fuse
FPGAs….[1]
Table 2.2 Summary of Commercially Available FPGAs

## Slide 10
TAB
(Taped Automated Bonding)
PQFP
(Plastic Quad Flat Package)
PLCC
(Plastic Leaded Chip Carrier)
DIP
(Dual In-line Package)

## Slide 13
The Design Warrior’s Guide to FPGAs Devices, Tools, and Flows. ISBN 0750676043 Copyright © 2004 Mentor Graphics Corp. (www.mentor.com)
General structure of an FPGA

## Slide 16: Field-Programmable Gate Arrays
Logic blocks
  to implement combinational and sequential logic
Interconnect
  wires to connect inputs and outputs to logic blocks
I/O blocks
  special logic blocks at periphery of device for external connections
Key questions:
  how to make logic blocks programmable?
  how to connect the wires?
  after the chip has been fabbed

## Slide 17: General FPGA chip architecture
a.k.a. CLB -- “configurable logic block”
Rissacher EE365
Lect #14

## Slide 18
The Design Warrior’s Guide to FPGAs Devices, Tools, and Flows. ISBN 0750676043 Copyright © 2004 Mentor Graphics Corp. (www.mentor.com)
Xilinx Spartan 3 FPGAs

## Slide 19: Spartan-II FPGA Family
DLL: Delay Locked Loop

## Slide 20: Island Style Architecture

## Slide 21
Interconnect Resources
Logic Block
I/O Cell
CONCEPTUAL FPGA

## Slide 22
Switch Boxes
Fs, defines for a wiring segment entering the S block the number of other wiring segments it can be connected to
Notes: The S boxes allow wires to switch between vertical and horizontal wires. Its flexibility, Fs, defines for a wiring segment entering the S block the number of other wiring segments it can be connected to. The topology of the S blocks is very important since it is possible to choose two different topologies with the same flexibility Fs that result in very different routabilities. For example, this figure shows that meanwhile topology 1 can’t connect wire A with B, topology 2 can.

## Slide 23
Routings using C and S Boxes

## Slide 24: Routing Algorithms
Maze Router
A* Search Routing
The Pathfinder

## Slide 27: Xilinx Virtex Architecture
Basic cell of the Virtex FPGA is configurable logic block(CLB)
CLB contains circuitry that allows it to efficiently perform arithmetic
LUT’s can be configured as SRAM cells
Contains programmable input output blocks (IOBs) interconnected to the CLBs

## Slide 28: FPGA - Field Programmable Gate Array
LB
Logic
Block
LB
Logic
Block
LB
Logic
Block
LB
Logic
Block
LB
Logic
Block
LB
Logic
Block
LB
Logic
Block
LB
Logic
Block
LB
Logic
Block
S/V
block
I/O
Cell
S/V
block
I/O
Cell
S/V
block
I/O
Cell
S/V
block
I/O
Cell
S/V
block
I/O
Cell
S/V
block
I/O
Cell
S/V block
I/O Cell
S/V block
I/O Cell
S/V block
I/O Cell
S/V block
I/O Cell
S/V block
I/O Cell
S/V block
I/O Cell

## Slide 29: The structure of FPGA

## Slide 30: Architecture of FPGA-s
LB
Symmetrical
Array
LB
LB
LB
LB
LB
LB
LB
LB
Row-based
LB
LB
LB
LB
LB
LB
LB
LB
LB
LB
Sea-of-Gates
LB
LB
LB
LB
LB
Hierarchical (CPLD)
PLA
PLA
PLA
PLA
PLA
PLA
PLA
PLA

## Slide 31: Logical block based on LUT-s
LUT
LUT
S
MUX
0
1
S
MUX
0
1
T
T

## Slide 32: Example: realisation of function based on MUX-s.
S
0
1
MUX
S
0
1
MUX
S
0
1
MUX
0
0
1
1
X1
X2
X3
X2
X3
Y
Y = X1 X2 + X1 X3
X1 X2 + X1 X3
X3
X2
1
0
0
1
X1 = 0
X1 = 1
X3 = 0
X3 = 1
X2 = 0
X2 = 1

## Slide 33: I/O cells
T
T
S/V contact
I/O pad
S
MUX
0
1
S
MUX
0
1

## Slide 35: Idealized FPGA Logic Block
4-input look up table (LUT)
  implements combinational logic functions
Register
  optionally stores output of LUT

## Slide 36
The Virtex CLB

## Slide 37: The Virtex CLB

## Slide 38: Details of One Virtex Slice

## Slide 40
x
y
COUT
0
0
1
1
0
1
0
1
y
y
CIN
CIN
Propagate = x  y
Generate = y
Sum= Propagate  CIN = x  y  CIN
x
y
Carry & Control Logic in Xilinx FPGAs

## Slide 41
Carry & Control Logic in Spartan 3 FPGAs
LUT
Hardwired (fast) logic

## Slide 42
Simplified View of Spartan-3 FPGA
Carry and Arithmetic Logic in One
Logic Cell

## Slide 43
Simplified View of Carry Logic in One Spartan 3 Slice

## Slide 44: Configurable Logic Blocks
A CLB can contain several slices, which make up a single CLB. Xilinx Virtex-5 FPGAs (right) have two slices: SLICEL (logic) and SLICEM (memory).
In addition to the basic CLB architecture, the Virtex-5 contains wide-function MUXs which can implement:
- 4:1 MUX using 1 LUT
8:1 MUX using 2 LUTs
16:1 MUX using 4 LUTs

## Slide 45
Implements any Two 4-input Functions
4-input function
3-input function;
registered

## Slide 46: Implement Some Larger Functions
e.g. 9-input parity

## Slide 47: Implements any 5-input Function
5-input function

## Slide 48: Two Slices: Any 6-input Function
6-input function
from other slice

## Slide 49: Fast Carry Chain: Add two bits per slice
Sum(a,b,cin)
Carry(a,b,cin)
a
b
cin

## Slide 50: Lookup Tables used as memory (16 x 2) [ Distributed Memory ]

## Slide 51: Lookup Tables used as memory (32 x 1)

## Slide 52: Virtex IOB

## Slide 53: Xilinx Virtex-5 FPGAs
Multi-FPGA-based emulation framework for NoC design and verification (UNLV Networking and System Integration Laboratory)

## Slide 54: Virtex-5 CLB
A single CLB in Virtex-5 consists of two slices: SLICEL (logic) and SLICEM (memory). Each CLB is connected to a switch matrix which can access to a general routing (global) matrix.
Every slice contains four LUTS, wide function MUXs, carry logic, and configurable memory elements. SLICEM support storing data using distributed RAM and data shifting with 32-bit shift registers

## Slide 55: SLICEL

## Slide 56: SLICEM

## Slide 57: FPGA Design Comparison Virtex-5, Virtex-6, and spartan 6
Virtex-6 CLB have the same setup as Virtex-5 (SLICEL & SLICEM)
Virtex-6 devices add four additional storage elements which can only be configured as edge-triggered D-FFs. The D inputs are driven by the output of the LUTs or bypass slice inputs AX-DX

## Slide 60: FPGA structure

## Slide 61: Simplified CLB Structure

## Slide 62: Example: 4-input AND gate
A | B | C | D | O
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1

## Slide 63: Example 2: Find the configuration bits for the following circuit
A0 | A1 | S | 
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 64: Interconnection Network

## Slide 65: Example 3
Determine the configuration bits for the following circuit implementation in a 2x2 FPGA, with I/O constraints as shown in the following figure. Assume 2-input LUTs in each CLB.

## Slide 66: CLBs required

## Slide 67: Placement: Select CLBs

## Slide 68: Routing: Select path

## Slide 69: Configuration Bitstream
The configuration bitstream must include ALL CLBs and SBs, even unused ones
CLB0: 00011
CLB1: 01100
CLB2: XXXXX
CLB3: ?????
SB0: 000000
SB1: 000010
SB2: 000000
SB3: 000000
SB4: 000001

## Slide 70: Realistic FPGA CLB: Xilinx

## Slide 71: XC 4000
XC4000 CLB
3 LUTs and 2 Flip-flops in a two stage arrangement
2 Outputs: Can be registered or combinational
External signals can also be registered
More of internal signals are available for connections
Can implement any two independent functions of four variables or any single function of five variables

## Slide 72: Xilinx FPGAs (IOB detail)

## Slide 73: XC4000E I/O Block
Rissacher EE365
Lect #14

## Slide 84: Xilinx 4000-series FPGAs
Rissacher EE365
Lect #14

## Slide 85: Xilinx Virtex-II Pro Development System
Notes: Has 2 Physical Power PC Cores

## Slide 86: Xilinx Virtex-II Pro Development System Logic and FPGA Interaction
Notes: Top: Block Diagram of the Virtex-II System
LEFT Side: Ways to configure the FPGA, Power the FPGA, Manage Clocking of the FPGA
RIGHT Side: Components/Peripherals and Outputs that can be utilized by the FPGA
Bottom: I/O pad connections to the Peripheral Devices

## Slide 87: Xilinx Virtex 5 Development System (Front)
Notes: Unlike the Virtex 2 the Virtex 5 uses a MicroBlaze processor; it is entirely software-based. Designed for Xilinx FPGAs from Xilinx. As a soft-core processor, MicroBlaze is implemented entirely in the general-purpose memory and logic fabric of Xilinx FPGAs

## Slide 88: Xilinx Virtex 5 Development System (Back)

## Slide 89: Xilinx Spartan-3E Starter Kit
FPGA
switches
buttons
LEDs

## Slide 90: Virtex 5 Development System Components (FPGA)
Configurable Logic Blocks
Array (Row*Column): 160*54
Virtex 5 Slices: 17,280
Max Distributed RAM (Kb): 1,120
Block RAM Blocks
18Kb: 296
36Kb: 148
Max (Kb): 5,328
DSP48E Slices: 64
CMTs: 6
PowerPC Processor Blocks: 0
In Comparison to the Virtex 2
Configurable Logic Blocks
Array (Row*Column): 80*46
Virtex 2 Slices: 13,969
Max Distributed RAM (Kb): 428
Block RAM Blocks
Max (Kb): 2,448
Notes: 1. Virtex-5 FPGA slices are organized differently from previous generations. Each Virtex-5 FPGA slice contains four LUTs and four flip-flops (previously it was two LUTs and two flip-flops.)
2. Each DSP48E slice contains a 25 x 18 multiplier, an adder, and an accumulator.
3. Block RAMs are fundamentally 36 Kbits in size. Each block can also be used as two independent 18-Kbit blocks.
4. Each Clock Management Tile (CMT) contains two DCMs and one PLL.
5. This table lists separate Ethernet MACs per device.
6. RocketIO GTP transceivers are designed to run from 100 Mb/s to 3.75 Gb/s. RocketIO GTX transceivers are designed to run from 150 Mb/s to
6.5 Gb/s.
7. This number does not include RocketIO transceivers.
8. Includes configuration Bank 0.
DCM: Digital Clock Manager
A phase-locked loop or phase lock loop (PLL) is a control system that generates a signal that has a fixed relation to the phase of a "reference" signal. A phase-locked loop circuit responds to both the frequency and the phase of the input signals, automatically raising or lowering the frequency of a controlled oscillator until it is matched to the reference in both frequency and phase. A phase-locked loop is an example of a control system using negative feedback.
In simpler terms, a PLL compares the frequencies of two signals and produces an error signal which is proportional to the difference between the input frequencies. The error signal is then low-pass filtered and used to drive a voltage-controlled oscillator (VCO) which creates an output frequency. The output frequency is fed through a frequency divider back to the input of the system, producing a negative feedback loop. If the output frequency drifts, the error signal will increase, driving the frequency in the opposite direction so as to reduce the error. Thus the output is locked to the frequency at the other input. This input is called the reference and is often derived from a crystal oscillator, which is very stable in frequency.

## Slide 91: Programming Environment (ISE Simulator)
ISE Foundation (Project Navigator) allows for the start of the FPGA design process
Runs in background to maintain operation and flow of design by managing the chain of tools involved including but not limited to: Embedded Development Kit (EDK), ChipScope Pro and AccelDSP
EDK consists of XPS as mentioned before this can be run independently to begin a project however use of the project navigator provides for a more organized design process of an embedded system

## Slide 92: Recommended Tool Set
Design Entry
  HDL Designer / Active HDL / Text Pad
Simulation
  ModelSim / Active HDL / NC Sim
Synthesis
  XST / Amplify / Synplify
Place & Route
  ISE

## Slide 93
Features | Artix-7 | Kintex-7 | Virtex-7 | Spartan-6 | Virtex-6
Logic Cells | 352,000 | 480,000 | 2,000,000 | 150,000 | 760,000
BlockRAM | 19Mb | 34Mb | 68Mb | 4.8Mb | 38Mb
DSP Slices | 1,040 | 1,920 | 3,600 | 180 | 2,016
DSP Performance (symmetric FIR) | 1,248GMACS | 2,845GMACS | 5,335GMACS | 140GMACS | 2,419GMACS
Transceiver Count | 16 | 32 | 96 | 8 | 72
Transceiver Speed | 6.6Gb/s | 12.5Gb/s | 28.05Gb/s | 3.2Gb/s | 11.18Gb/s
Total Transceiver Bandwidth (full duplex) | 211Gb/s | 800Gb/s | 2,784Gb/s | 50Gb/s | 536Gb/s
Memory Interface (DDR3) | 1,066Mb/s | 1,866Mb/s | 1,866Mb/s | 800Mb/s | 1,066Mb/s
PCI Express® Interface | Gen2x4 | Gen2x8 | Gen3x8 | Gen1x1 | Gen2x8
Agile Mixed Signal (AMS)/XADC | Yes | Yes | Yes |  | Yes
Configuration AES | Yes | Yes | Yes | Yes | Yes
I/O Pins | 600 | 500 | 1,200 | 576 | 1,200
I/O Voltage | 1.2V, 1.35V, 1.5V, 1.8V, 2.5V, 3.3V | 1.2V, 1.35V, 1.5V, 1.8V, 2.5V, 3.3V | 1.2V, 1.35V, 1.5V, 1.8V, 2.5V, 3.3V | 1.2V, 1.5V, 1.8V, 2.5V, 3.3V | 1.2V, 1.5V, 1.8V, 2.5V
EasyPath Cost Reduction Solution | - | Yes | Yes | - | Yes
FPGA Comparison Table